## Slide 1: Command motion using moveit2 & CML
Anthony Redamonti

## Slide 2: moveit2 Overview
  Robotic manipulation platform for ROS2 (open-source robotics middleware suite)
  Features the latest advances in Motion Planning, Manipulation, 3D Perception/Visualization, Kinematics, Control, and Navigation

## Slide 3: moveit2 plugin in rviz
Easy to use GUI to plan and execute trajectories!

## Slide 4
rclcpp: ROS Client Library for C++
  C++ API for interacting with ROS
  Provides similar features as the RVIZ plugin
  Your First C++ MoveIt Project

## Slide 5: 1. Target pose
      Specify X,Y,Z coordinates and orientation of end-effector
// create a target pose for the robot geometry_msgs::msg::Pose target_pose; target_pose.orientation.w = 1.0; target_pose.position.x = 0.2; target_pose.position.y = 0.2; target_pose.position.z = 0.5; move_group_interface.setPoseTarget(target_pose);

## Slide 6: 2. Create a plan
      Ask MoveIt to create a plan to the target pose
// create a plan to the target pose moveit::planning_interface::MoveGroupInterface::Plan my_plan; success = (move_group_interface.plan(my_plan) == moveit::planning_interface::MoveItErrorCode::SUCCESS);

## Slide 7: 3. Extract the trajectory
      Get the list of commanded positions from the trajectory in the plan
// get the trajectory from the plan moveit_msgs::msg::RobotTrajectory msg = my_plan.trajectory_; std::vector<int>::size_type totalNumPvtPoints = msg.joint_trajectory.points.size(); printf("\nThe total number of PVT points = %ld", totalNumPvtPoints);

## Slide 8: 3. Extract the trajectory (cont.)
// extract all PVT data for (unsigned i=0; i<totalNumPvtPoints; i++) { printf("\nPVT point = %d", i); std::vector<double> pvtPoint; // get the size (how many axes are in PVT point) std::vector<int>::size_type size2 = msg.joint_trajectory.points[i].positions.size(); for (unsigned j=0; j<size2; j++) { float radFloat = msg.joint_trajectory.points[i].positions[j]; printf("\nAxis %d radians: %g", j, radFloat); float degrees = (180/PI_VALUE) * radFloat; // convert radians to degrees printf(" degrees: %g", degrees); degrees = degrees / 360.0; // 360 degrees in one rev double counts = degrees * (countsPerRevArr[j] * 1.0); // convert degrees to encoder counts printf(" counts: %f", counts); pvtPoint.push_back(counts); // record the starting position if(i == 0){ startingPos[j] = counts; } } // add the PVT point to the PVT constant acceleration object err = pvtConstAccelTrjObj.addPvtPoint(&pvtPoint, &timeBetweenPoints); showerr( err, "adding PVT point to pvtConstAccelTrjObj" ); }

## Slide 10: Thank You
aredamonti@copleycontrols.com